Planar Projections: subclasses are based on the orientation of the object with respect to the projection plane

Planar Projections

Perspective Projections

Parallel Projections

One-Point

Two-Point

Three-Point

Oblique

Orthographic

Cavalier

Cabinet

General

Multiview

Axnometric

Isometric

Dimetric

Trimetric

Classes of Parallel Projections

Oblique – used when one object face is significantly more complicated than the other faces of the object; one principal face of the object is parallel to the projection plane and is projected true size; an in plane angle beta (the 30 degree angle we draw) measures the angle of rotation of the projector about the projection plane normal. The out – of plane angle alpha is called the oblique projection angle and it determines the type of oblique projection, cavalier cabinet or general
- Cavalier Oblique: the oblique projection angle used is 45 degrees, the projection of depth seems elongated; the receding axis is not foreshortened but scaled the same as the horizontal and vertical principal axes
- Cabinet Oblique: the oblique projection angle is approximately 63.43 degrees; the projected receding edge length is one half that of the other edge lengths; the receding axis is foreshortened to exactly one half of the other principal axes
- General Oblique: the oblique projection angle is between 445 and 63.43 degree; the receding axis is scaled between ½ and 1
Orthographic Projection – most commonly used for engineering; differs from oblique projection in that the parallel projectors are perpendicular (normal) to the projection plane;
Axonometric: all three principal axes are inclined to the projection plane (no axis is parallel or perpendicular to the projection plane); when projected, three principal faces of the object are visible - results in an orthographic pictorial view
- Trimetric Projection: none of the angles between the projected principal axes are equal; all three axes are foreshortened by different amounts
- Dimetric: two of the three angles are equal; two fo the three projected axes are foreshortened the same amount
- Isometric Projection: all three angles are equal; all axes are foreshortened the same amount; in an isometric projection, each principal axis is foreshortened to approximately 82% of its true length (an isometric projection without foreshortening is refereed to as an isometric drawing – it is larger than a true isometric projection)

Multiview: one object face and two principal axes are parallel to the projection plane; when projected, only one object face is visible; identical to oblique projection, as well as one-point perspective projection;
Projectors are parallel to one another; projectors are normal to the projection plane; object is positioned with one principal face parallel to the projection plane

Isometric Lines: lines parallel to a principal axis
Nonisometric Lines: not parallel to any of the three principal axes
An objects longest principal dimension should appear as a horizontal dimension on the front face of the object.

Third Angle Projection: used in the US, Great Britain, assumes that an object to be projected resides in the third quadrant; the projection planes are between the viewer and the object ; glass box opens towards you
First Angle Projection: used in the rest of Europe and Asia, the object to be projected is placed in the first quadrant; the projection plane are all placed behind or below the object
Continuous Lines Represent: edge view of a surface, edge between two intersecting surfaces, extent of a contoured surface

limiting elements of a hole
Centerlines: typically extend about 5 mm beyond the feature being represented; represent the axis of a cylinder or hole
Line Precedence: visible, hidden, center
Normal Surface: a planar surface that is orthogonal to the principal planes; appears as a true-size surface in a three-view drawing
Inclined Surface: a normal surface that has been rotated about a line parallel to a principal axis perpendicular to one principal plane; appears foreshortened in two views, while in the third view it appears on edge (length is true length)

Auxiliary View: an orthographic view that is projected onto any plane other than one of the principal planes
Primary Auxiliary View: projected onto a plane perpendicular to one of the principal planes, and inclined to the other two (can be used ot find the true size and shape of an inclined surface)
Secondary Auxiliary View: projected from a primary auxiliary view onto a plane that is inclined to all three principal projection planes (can be used to find the true size and shape of an oblique surface)
Full Section: the cutting plane passes all the way though the object
Half Sections: the cutting plane only passes half way through the part
Offset Section: a modified full section that is used when important internal features do not lie in the same plane, the cutting plane is stepped, or offset in order to pass through these features
Broken out Section: when only a portion of the part needs to be sectioned; a jagged or freehand break line is used to separate the sectioned from the unsectioned portion of the drawing; show internal and external features in the same view
Revolved Section: created by passing a cutting plane perpendicular to the center place of an elongated symmetrical feature and then revolving the resulting cross-section 90 degrees into the plane of the drawing
Removed Section: cross-section is not superimposed on the view like a revolved section but rather is placed at some convenient location; used whent here is insufficient room for a revolved section
- Main goals of dimensioning:
  - Use only the dimensions needed to completely define the part, no more
  - Select and arrange dimensions to support the function and mating relationship of the part; it is important that the dimensioned part not be subject to differing interpretations
  - Do not specify the manufacturing methods to be used in building the part
  - Arrange the dimensions for optimum readability
  - Unless otherwise stated, assume angles to be 90 degrees
- Aligned dimensioning is not recognized by ANSI
- A distance of 10 mm between the first dimension line and the part, and an additional 6 mm for the following lines
- Dimensioning Rules and Guidelines
  - Prisms: do not repeat dimensions; apply dimensions to a feature in its most descriptive view; dimension between views; omit one (intermediate) dimension; place smaller dimensions inside larger dimensions; dimension to visible object lines, not to hidden lines; keep dimensions outside the views; extension lines may cross object lines and other extension lines; dimension the diameter of cylindrical parts in their rectangular view; dimension the diameter of cylindrical holes in their circular view; dimension the radius of circular arcs in the view where their true shape is seen
- Solid part models are rigid bodies and consequently have six degrees of freedom, three in translation and three in rotation
- Initially, all six degrees of freedom are open – removing these DoFs, the part’s freedom is to translate and/or rotate is limited, either partially or completely
- Assembly constraints are paramentric constraints that restrict a part’s motion relative to ]another part, by removing DoFs (i.e. mate and insert)